## Slide 1: Final Session

## Slide 2: Course Summary
Main topics:
  Master QGIS GUI
  How to install/ update Plugins
  Load vector data from various sources
  Cartography: Symbology, Label
  Understand Coordinate Reference System and how it works in QGIS (define custom projection, Reproject)
  Working with Attribute Table: view, query, calculate field,..
  Working with spatial features: edit features, spatial query, spatial analysis, spatial processing
  Search Processing Toolbox by appropriate keywords
  Map Layout Composer

## Slide 3: Course Summary
Tip and Tricks:
  How to use Bookmarks
  Use HCMGIS Plugin for Basemaps, download free and open geospatial data, convert (Vietnamese) Font, define custom Projections, merge/ split layers, merge/ split fields, some geometry processing tools based on Voronoi Diagram.
  Advanced Digitizing Toolbar: Only available in projected CRS
    Construction Mode
    Parallel
    Perpendicular
    Lock and continuous lock X, Y, Angle, Distance when editing

## Slide 4: Course Summary
Useful shortcut keys:
  F1: Access QGIS User Guide
  F2: Rename active layer
  F3: Select Features by Value
  F5: Refresh
  F6: Open Attribute Table
  F11: Toggle Full Screen Mode
  Crtl + Tab: Toggle Panels Visibility
  Crtl + Ship + Tab: Toggle Map Only
  Crtl + K: QGIS Locator Bar (search for algorithms, actions and layer names, select a feature in current active layer by typing an attribute value.)

## Slide 5: Course Summary
Final Exam:
  Reproject all the wards, roads and hospitals layer to VN – 2000 Projection of HCMC.
  Symbology the ward layer by ward name
  Label the road with level 1, 2 by road name
  Split the hospitals layer to 14 layers by ward name
  Clip and extract the road of “Phường 7”
  Calculate the population density of each ward (using pop.xlsx)
  Find the shortest and longest road
  Convert all the attribute in wards layer to UPPER CASE and without accents characters.

## Slide 6: Course Summary
Discussion

## Slide 7: Course Summary
Congratulations for Achievement